## Slide 1
Colombia Employment Factors
Reusable employment-factor data and learning-curve methodology for power-sector models
Purpose
Separate labour-impact assumptions from the optimization model and expose them as an installable Python package.
Current dataset
193 rows
22 technologies
Years: 2015, 2024, 2030, 2050
OSeMOSYS
TIMES-MARKAL
LEAP
Ex-post jobs
Just transition
1

## Slide 2
Why A Separate Package?
Employment factors are model-agnostic; model outputs are model-specific.
Separation of concerns
OSeMOSYS solves the energy system. This package computes labour impacts from the solved capacities.
Independent versioning
Employment assumptions can evolve without changing the core model repository.
Reusable interface
The same factor table can support OSeMOSYS, TIMES-MARKAL, LEAP, or spreadsheet workflows.
Package boundary
Inputs: technology, year, capacity, factor filters.
Outputs: jobs or job-years by source, factor type, and job type.
Adapters translate model-specific names and columns into this neutral structure.
2

## Slide 3
Repository Structure
The refactor separates reusable code, source data, generated outputs, and model adapters.
src/colombia_employment_factors
Installable package: formulas, mappings, projections, employment_factors.py, adapters.
data/raw
Original curated employment-factor CSV.
data/processed
Model-ready long-format employment factors.
data/audit
Excel workbook for traceability and review.
scripts/
Maintainer commands that rebuild outputs from raw inputs.
tests/
Formula checks, projection checks, and OSeMOSYS adapter checks.
docs/sources/
Source PDFs and catalogue files used for methodology documentation.
3

## Slide 4
Employment Factor Table
The processed data is long-format so it can be filtered and joined to model outputs.
Core dimensions
Source
Technology
Factor_Type
Job_Type
Unit
Year
Value_Numeric
Projection metadata
Method_Applied
Mapped_Rutovitz_Tech
Rutovitz_2030_Factor
Mapped_Catalogue_Tech
Learning_Rate
Projection_Input
Base_Year and Projected_Year
4

## Slide 5
Rutovitz 2015 Decline Factors
Construction and manufacturing rows from Rutovitz 2015 are brought to 2030 with Table 9 factors.
Formula
EF_2030 = EF_2015 * (1 + decline_2030)
The coefficient is technology-specific and uses the Latin America 2030 value from Rutovitz Table 9.
Scope
Applied only to Construction and Manufacturing factors.
O&M and fuel rows remain as original values unless separately updated by source data.
Examples: Coal uses multiplier 0.75; Solar PV uses 1.41; Offshore wind uses 1.23; Hydro large/small use 0.94.
5

## Slide 6
Learning-Curve Method
2024 construction and manufacturing-related rows are projected to 2030 and 2050 using cumulative capacity growth.
projected_factor = base_factor * capacity_ratio ^ log2(1 - learning_rate)
Equivalent spreadsheet exponent: LN(1 - LR) / LN(2)
Variables
base_factor: 2024 employment factor
capacity_ratio: accumulated generation capacity relative to 2024
learning_rate: technology learning rate from the Colombian catalogue mapping
Interpretation
As cumulative capacity increases, labour intensity per MW falls for technologies with positive learning rates.
The approach mirrors the standard cost learning curve, applied to employment intensity.
6

## Slide 7
Catalogue Mapping And Fallbacks
Technology names are mapped to catalogue categories; missing learning inputs use explicit CAPEX-ratio fallback rules.
Direct learning-rate mappings
Solar PV -> Solar PV
Onshore wind -> Wind onshore
Offshore wind -> Wind offshore
Hydro large/small -> Hydro
Biomass power -> Bioenergy
Battery storage -> Battery storage
CAPEX-ratio fallback
EF_t = EF_2024 * (CAPEX_t / CAPEX_2024)
Used where no catalogue learning-rate/capacity-ratio mapping was available.
Examples: Coal, Natural Gas, Nuclear, and Oil/Diesel proxy treatment.
7

## Slide 8
Projection Workflow
The package keeps every projected row auditable through method and mapping metadata.
1. Read base factors
Load the curated long-format 2015 and 2024 employment-factor table.
2. Apply method
Rutovitz Table 9, learning curve, or CAPEX fallback depending on source and technology.
3. Write outputs
Generate processed CSV plus audit workbook with mappings and formula context.
Output rows preserve Source, Technology, Factor_Type, Job_Type, Unit, Year, Value_Numeric, and projection metadata.
8

## Slide 9
OSeMOSYS Integration
The package is designed for ex-post calculations after the OSeMOSYS optimization has solved.
Model output
OSeMOSYS exports technology-year capacity results such as NewCapacity.
Adapter
The OSeMOSYS adapter maps model technology names to employment-factor technology names.
Jobs calculation
Employment = model_capacity * employment_factor
Python API
from colombia_employment_factors import get_employment_factors
from colombia_employment_factors.adapters.osemosys import calculate_capacity_jobs
factors = get_employment_factors()
jobs = calculate_capacity_jobs(results, factors)
9

## Slide 10
Quality And Traceability
The refactor adds repeatability without hiding assumptions.
Tests
Learning-curve formula equals the Excel LN expression.
Projection rows are checked against known values.
OSeMOSYS adapter merge and multiplication are checked.
Audit trail
Generated rows include method, mapped technology, learning rate, and projection input.
Raw, processed, audit, and source folders have distinct responsibilities.
Assumptions remain visible for future UPME review.
10

## Slide 11
Recommended Next Steps
The package is ready for GitHub publication and downstream model integration.
1. Replace approximate CAPEX fallback ratios with fully extracted catalogue values where possible.
2. Add a documented OSeMOSYS-UPME technology-name mapping file.
3. Add citation guidance for Rutovitz, the Colombian Technology Catalogue, and derived outputs.
4. Tag a first release and reference it from OSeMOSYS-UPME requirements.txt.
5. Add examples for TIMES-MARKAL or other models only through separate adapters.
11